## Slide 1: 2015 SAFETY SEMINAR
HIGHLIGHTS OF 2014
Rick Moses
Chief, Bureau of Safety
Florida

## Slide 2: Violation Notices
Highlight details:
1. 258 PHMSA and 172 PSC violations issued.
2. 144 PHMSA and 100 PSC violations
resolved.
3. Progress evaluations conducted on
179 PHMSA and 133 PSC violations.
4. 35 PHMSA and 34 PSC non-closure letters
sent.
Notes:   substantial and measureable
  formal commission action and/or well documented settlements
  cost or penalty born by the shareholder not ratepayer
  Example: Passed a state law requiring all inactive gas lines be cut off at the main in 5 years after inactivity.
  Example: Require cast iron frost surveys weekly in business districts during frost conditions

## Slide 3: Top Enforcement Issues in 2014
1. Public Awareness
2. Procedural Manual
3. Atmospheric Corrosion Control
4. Pressure Limiting and Regulating Stations
5. Criteria for Cathodic Protection
Notes: These should be notable items, if there are any. No need to list routine issues such as “missing documentation” unless it became systemic or otherwise notable in 2014.
Example: Damage prevention, late on rectifier reads and repairs, person performing odorant checks no OQ, no documented pressure tests, etc.

## Slide 4: Upcoming Rule Changes
25-12.005 Codes and Standards Adopted 25-12.008 New, Reconstructed or converted Facilities | Change the year of the code from 2011. | Adopt new code year
25-12.022 Requirements for Distribution System Valves | Substitute the word “emergency” for Sectionalizing. | This change would include ‘valves ahead of regulator stations’ and ‘blowdown valves’ in the requirement as they are all valves that are to be used in an emergency.
25-12.030 Construction Inspection | Remove wording allowing a person who worked on the main to inspect it. | Newly amended PHMSA rule 192.305 will not allow this (as of 3/11/15.)
25-12.040(3) Leak Surveys, Procedures and Classification | Clarify how many rechecks are to be done ( until there is zero residual gas) | The rule states ‘recheck’ and does not mention what to do if the recheck still detects residual gas in the ground.
25-12.085(1) Written Annual Reports Required | Change the year of the report from 12-05. | PHMSA modified the form
25-12.085(2) Written Annual Reports Required | Remove this section. | Redundant with (3) and does not have the full transmission definition. 25-12.085(3) already refers to a transmission system which would include distribution companies.
25-12.085(3) | Change the year of the report from 12-05. | PHMSA modified the form

## Slide 5: Incident Reporting Change
Change O&M to delete reference to reporting and incident to the NRC via the website.
The website is no longer operational.
Use 800/424-8802 to report incidents to NRC.