## Slide 1
Florida Public Service Commission 2013 Ten-Year Site Plan Workshop FRCC Presentation
Stacy Dochoda President and CEO
September 25, 2013

## Slide 2: Agenda
Executive Summary
FRCC Load & Resource Plan
  Load Forecast, Generation Additions, Reserve Margins, Fuel Mix
  Renewable Resources and Demand Side Management (DSM)
FRCC Fuel Reliability
  Natural Gas Energy Production in Florida
  Natural Gas Infrastructure in Florida
FRCC Transmission Planning
  FRCC Regional Transmission Planning Process
  Crystal River Unit Retirements
  Status of FERC Order 1000
2

## Slide 3: Florida Reliability Coordinating Council
The purpose of the
Florida Reliability Coordinating Council is to
promote and enhance
the reliability and adequacy
of the bulk electricity supply in Florida,
now and into the future.
3

## Slide 4: Executive Summary
Planned Reserve Margins > 20% (although resource mix is changing towards greater dependency upon Demand Side Management resources)
Demand Response1/ reduces load (MW) at peak by 7% throughout the 10-year horizon
Utility-sponsored Energy Efficiency/Energy Conservation programs reduce load (MW) at peak by 2.8% by 2022
Additional Energy Efficiency delivered through mandated codes and standards accounted for in load forecast reduces load (MW) at peak by at least 3.7% by 2022
Renewables are 3,150 GWh (1.2%) of energy served by 2022
4
1/Demand Response = Load Control + Interruptible programs; i.e. dispatchable DSM

## Slide 5: Executive Summary (Continued)
Energy production from natural gas expected to increase 13.2% by 2022
96% of the gas pipeline capacity into Florida is subscribed
Impact of EPA regulations:
  RICE1/ rule projected to negatively impact Commercial/Industrial Demand Response projections
  Prospective 2015 retirements at Crystal River due to MATS2/ would have transmission impacts
  Mitigation plans are being developed
5
1/RICE: Reciprocating Internal Combustion Engine
2/MATS: Mercury and Air Toxics Standard
Notes: From LTRA
In addition, in 2010 EPA issued national emission standards for hazardous air pollutants (NESHAP) for existing compression ignition reciprocating internal combustion engines (RICE), i.e., diesel generators, which must comply with the rule beginning May 3, 2013. The RICE NESHAP imposes stringent emission limits and other requirements on non-emergency RICE. As amended in January 2013, it also imposes hourly limits on the operation of emergency RICE in non-emergency situations, including for emergency demand response, local system reliability, peak shaving (not allowed at all after May 3, 2014), and other non-emergency operation. It is still unknown the full impact that CSAPR and its replacement rule, MATS, and the RICE NESHAP will have on the long range reliability of the BES in the FRCC region.

## Slide 6: FRCC Load & Resource Plan
6

## Slide 7: Load Forecast Factors
Florida unemployment (actual) continues to decrease
Population continues to pick up momentum
Florida’s Gross State Product (GSP) levels lower than expected in 2011-12; new projections show slightly slower recovery
Forecasted energy sales and peak demands are lower in 2013 TYSP compared to 2012 TYSP
7
Notes: (This table is available on a back up slide)

## Slide 8
Comparison of 2012 vs. 2013
FRCC Firm Peak Demand Forecast (Summer)
Chart: Projected Year
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
2012 | 43041 | 43618 | 44459 | 45242 | 45802 | 46152 | 46803 | 47581 | 48273
2013 | 42532 | 43142 | 43812 | 44355 | 44907 | 45457 | 46125 | 46808 | 47538
Notes: (This graph is available on a back up slide)

## Slide 9
Comparison of 2012 vs. 2013 FRCC Firm Peak Demand Forecast (Winter)
Chart: Projected Year
| 13/14 | 14/15 | 15/16 | 16/17 | 17/18 | 18/19 | 19/20 | 20/21 | 21/22
2012 | 44015 | 44228 | 44790 | 45297 | 45752 | 46305 | 46910 | 47509 | 48169
2013 | 43384 | 44060 | 44596 | 45074 | 45543 | 46105 | 46675 | 47259 | 47870
Firm Peak Demand (MW)
1

## Slide 10
Comparison of 2012 vs. 2013 FRCC Net Energy for Load Forecast
Chart: Projected Year
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021
2012 | 227095 | 230481 | 235490 | 239191 | 242626 | 245696 | 249324 | 254024 | 259024
2013 | 225384 | 229771 | 233937 | 237569 | 240276 | 243012 | 245932 | 249183 | 251942
Net Energy for Load (GWh)
1

## Slide 11: FRCC Region Compound Average Annual Growth Rate1/ for Load (MW)
Chart: Year
| 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013
Summer Growth Rate (%) | 2.17 | 2.19 | 2 | 2.05 | 1.8 | 1.86 | 1.98 | 2.05 | 2.17 | 2.36 | 2.61 | 2.44 | 2.52 | 2.52 | 2.74 | 2.42 | 2.24 | 2.14 | 1.82 | 1.27 | 1.54 | 1.44 | 1.44
Winter Growth Rate (%) | 2.67 | 2.36 | 2.3 | 2.61 | 2.21 | 1.97 | 2.13 | 2.23 | 2.33 | 2.34 | 2.43 | 2.37 | 2.57 | 2.59 | 2.69 | 2.4 | 2.27 | 2.09 | 2.07 | 1.56 | 1.27 | 1.12 | 1.29
1/Projected growth rate from prior forecasts

## Slide 12
FRCC Summer Peak Demands
Actual and Forecasted
Chart: Year
| 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Actual Peak Demand | 27238 | 27662 | 28930 | 29748 | 29321 | 31801 | 32315 | 32924 | 37153 | 37493 | 37379 | 38670 | 39903 | 40417 | 42172 | 45924 | 45344 | 46525 | 44706 | 46260 | 45564 | 44777 | 44338 | 45668 | 46338 | 47053 | 47650 | 48285 | 48881 | 49603 | 50336 | 51110 | 51968
Forecasted Peak Demand | 45668 | 46338 | 47053 | 47650 | 48285 | 48881 | 49603 | 50336 | 51110 | 51968
Linear Trend (Actual Peak Demand) | 27484.6848 | 28450.7569 | 29416.8291 | 30382.9012 | 31348.9733 | 32315.0455 | 33281.1176 | 34247.1897 | 35213.2619 | 36179.334 | 37145.4061 | 38111.4783 | 39077.5504 | 40043.6225 | 41009.6947 | 41975.7668 | 42941.8389 | 43907.9111 | 44873.9832 | 45840.0553 | 46806.1275 | 47772.1996 | 48738.2717 | 49704.3439 | 50670.416 | 51636.4881 | 52602.5603 | 53568.6324 | 54534.7045 | 55500.7767 | 56466.8488 | 57432.9209 | 58398.9931

## Slide 13: Load & Resource Plan Total Available Capacity (Summer)
Chart: Year
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Utility-Owned Capacity (Inside Region) | 47388.9 | 47388.9 | 47388.9 | 47388.9 | 47388.9 | 47388.9 | 47388.9 | 47388.9 | 47388.9 | 47388.9
Utility-Owned Capacity (Outside Region) | 836 | 836 | 836 | 836 | 836 | 836 | 836 | 836 | 836 | 836
Net Changes to Utility-Owned Capacity | 0 | 1142.2 | 2018.2 | 2207.0001 | 2206.6 | 3252.5999 | 3224.5999 | 4771.5999 | 5551.5999 | 7555.5999
Firm Non-Utility Purchases | 5167.69 | 4409.49 | 4480.99 | 6062.39 | 5945.84 | 5445.99 | 5268.44 | 4197.19 | 4146.54 | 3868.54
Imports (Purchased Power) | 1340 | 1340 | 1340 | 412 | 412 | 512 | 612 | 612 | 612 | 612
1/Existing generation as of December 31, 2012
1/
1/
Notes: Firm Non-Utility Purchases: - NUG , IPP , QF

## Slide 14: Load & Resource Plan FRCC Planned Reserve Margin
Chart: Year
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Summer | 28.6857 | 27.7562 | 27.9651 | 28.2974 | 26.4599 | 26.3513 | 24.2926 | 23.4953 | 23.1332 | 24.6118
Winter | 33.8404 | 36.8257 | 33.0491 | 36.1401 | 30.7803 | 33.7674 | 29.9538 | 34.0105 | 33.4678 | 33.8783
PSC Stipulation (IOUs) FRCC Criteria

## Slide 15: Load & Resource Plan FRCC Planned Reserve Margin (excluding projected DR)
Chart: Year
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
Summer
Winter
Summer | 19.8489 | 18.9447 | 19.1509 | 19.4256 | 17.6128 | 17.5006 | 15.5776 | 14.8397 | 14.5276 | 15.958
Winter | 24.99 | 27.8289 | 24.3338 | 27.1762 | 22.1193 | 24.9032 | 21.3386 | 25.1324 | 24.6679 | 25.1263
PSC Stipulation (IOUs) FRCC Criteria

## Slide 16
FRCC Demand Forecast (Summer)
Chart: Year
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
2013 (Firm Load with DR & EE/EC Excluded) | 45853.2 | 46683.4 | 47557.6 | 48308.8 | 49098 | 49844.2 | 50716.4 | 51579.6 | 52471.8 | 53450
2013 (Firm Load with DR Excluded) | 45668 | 46338 | 47053 | 47650 | 48285 | 48881 | 49603 | 50336 | 51110 | 51968
2013 (Firm Load) | 42532 | 43142 | 43812 | 44355 | 44907 | 45457 | 46125 | 46808 | 47538 | 48359
1/DR: Demand Response
2/Utility sponsored Energy Efficiency/Energy Conservation (EE/EC) programs only
2/
1/
1/
Notes: (This graph is available on a back up slide)

## Slide 17: Load & Resource Plan Generation-Only Reserve Margin1/
Chart: Year
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
FRCC | 19.3692 | 18.0689 | 17.8909 | 17.8011 | 15.759 | 15.3223 | 13.1309 | 12.16 | 11.6429 | 12.8289
FRCC Criteria

## Slide 18: Load & Resource Plan Demand Response as a Percentage of Peak Demand
Chart: Summer 2013
| MISO | FRCC | PJM | NPCC | SERC | WECC | SPP | ERCOT
 | 0.084154 | 0.068525 | 0.067655 | 0.039371 | 0.0383 | 0.027569 | 0.025809 | 0.02522
Source: NERC’s 2013 Summer Reliability Assessment (http://www.nerc.com/pa/RAPA/ra/Reliability%20Assessments%20DL/2013SRA_Final.pdf)

## Slide 19: FRCC Reliability Assessment Reserve Margin Review
Planned Reserve Margins expected to be greater than 20% (but are projected to be increasingly dependent upon all types of DSM)
FRCC has second highest amount of Demand Response as a percentage of a region’s peak load
19

## Slide 20: Fuel Mix (Energy)
Chart: 
| Nuclear | Coal | Oil | Gas | Other | NUG | Renewables
2017 NEL | 34439 | 48690 | 437 | 149825 | 17178 | 1523 | 3150
2013
225,384 GWh
2022
255,242 GWh
Chart: 
| Nuclear | Coal | Oil | Gas | Other | NUG | Renewables
 | 28268 | 44747 | 470 | 133523 | 13094 | 2174 | 3108
Net Energy for Load (GWh)
20
(16,302 GWh)
13.2% increase from Gas

## Slide 21: Fuel Mix (Capacity)
2013
53,535 MW
2022
59,792 MW
Summer Capacity1/ (MW)
Chart: 
| Nuclear | Coal | Oil | Gas | Renewables | Hydro
 | 0.067077 | 0.17315 | 0.13765 | 0.61017 | 0.011142 | 0.00081254
Chart: 
| Nuclear | Coal | Oil | Gas | Renewables | Hydro
 | 0.078455 | 0.14075 | 0.13669 | 0.62492 | 0.018456 | 0.00072752
1/Only accounts for firm capacity

## Slide 22: 2013 Existing Renewable Resource Capacity
Chart: 
| Biomass | Municipal Solid Waste | Heat Recovery | Solar | Hydro
 | 0.27842 | 0.32979 | 0.22307 | 0.12916 | 0.039485
1,380 MW
Summer Capacity1/ (MW)
1/ Contains non-TYSP data that includes both Firm and Non-Firm Capacity

## Slide 23: Renewables Forecast
Existing Renewables Capacity 1/ 1,380 MW
Planned Additions (through 2022) 1/
    Biomass 481 MW
    Municipal Solid Waste 125 MW
    Solar PV 2/ 333 MW
    Solar Projects (other) 31 MW
    TOTAL ~ 970 MW
1/ Contains non-TYSP data that includes both Firm and Non-Firm Capacity
2/ DEF: 310 MW; GRU: 21 MW; TAL: 2 MW

## Slide 24: Nuclear Outlook
Existing1/ Nuclear Capacity (Summer)
    St. Lucie 1 981 MW
    St. Lucie 2 989 MW
    Turkey Point 3 808 MW
    Turkey Point 4 693 MW
    Total 3,471 MW
Planned
    Turkey Point 4 2/ (uprate) 120 MW (3/2013)
    Turkey Point 6 (new) 1,100 MW (6/2022)
    Total 1,220 MW
1/ Existing capacity as of December 31, 2012
2/ Approximate MWs

## Slide 25: FRCC Load & Resource Assessment Conclusion
The FRCC Region has adequate total planned generation resources over the ten year period
Greater dependence upon DSM resources and additional analyses will be performed

## Slide 26: FRCC Fuel Reliability
26

## Slide 27: 2013 FRCC Fuel Reliability
Fuel Reliability Working Group (FRWG)
  Reviews existing interdependencies of fuel availability and electric reliability
  Coordinate regional responses to fuel issues and emergencies
27

## Slide 28
Energy Production from Natural Gas1/
Chart: Year
| 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022
ACTUAL | 34964 | 36650.9391 | 38835 | 53278 | 57964 | 67177 | 75753 | 90635 | 93157 | 94717 | 111508 | 120075 | 129378 | 140577
2013 Load & Resource Plan | 133523 | 136782 | 137720 | 139834 | 140448 | 144780 | 144029 | 150331 | 152868 | 149825
2012 Load & Resource Plan | 132641 | 133831 | 134419 | 135007 | 138399 | 142509 | 143881 | 149131 | 149145
1/ Extended nuclear outages for uprate work resulted in higher gas usage in 2012

## Slide 29: Ten Largest States for NG Consumption (2011 Data)
State | Total Annual Natural Gas Consumption (Bcf) | Annual NG Consumption for Electric Generation (Bcf) | Total Annual Marketed Natural Gas Production (Bcf) | Total Miles of Natural Gas Pipeline | Total Storage Capacity (Bcf)
Texas | 3,646 | 1,555 | 7,113 | 58,588 | 812
California | 2,153 | 651 | 250 | 11,770 | 571
Louisiana | 1,398 | 462 | 3,029 | 18,900 | 690
Florida | 1,218 | 1,050 | 15 | 4,971 | 0
New York | 1,217 | 427 | 31 | 5,018 | 246
Illinois | 987 | 50 | 2 | 11,911 | 997
Pennsylvania | 963 | 304 | 1,311 | 8,680 | 777
Ohio | 820 | 93 | 79 | 7,670 | 580
Michigan | 776 | 100 | 138 | 9,722 | 1,075
New Jersey | 661 | 188 | 0 | 1,520 | 0
Total US | 24,385 | 7,884 | 24,036 | 305,954 | 8,849
Florida as % of Total | 5.0% | 13.3% | 0.06% | 1.6% | 0%
FRCC entities maintain liquid fuel storage capability to provide service for an average of 4.8 days before replenishing

## Slide 30: Pipeline Delivery Capacity to State of Florida Contracted on a Firm Transportation Basis to Electric Generation Customers
The two major existing pipelines are more than 96% subscribed
Recently proposed 3rd gas pipeline by 2017 would enhance gas delivery reliability
Pipeline | Delivery Capacity (MMcf/d) | Approximate Delivery Capacity in Florida Held by Generators (MMcf/d) | Approximate Percentage of Capacity Held by Electric Generators
Florida Gas Transmission | 3,075 | 2,721 | 88%
Gulfstream Natural Gas | 1,300 | 1,255 | 97%
Southern Natural Gas Company | 121 | 65 | 54%
Gulf South Pipeline Company | 190 | 15 | 8%
Total Capacity into State of Florida | 4,686 | 4,056 | 87%

## Slide 31: Fuel Reliability Conclusions
Florida has greater natural gas demand than all but four states and greater natural gas demand to support generation than all states but Texas
Florida has minimal in-state production, no in-state storage and less miles of pipeline within the state than all but one of the ten largest gas consuming states
31

## Slide 32: Fuel Reliability Conclusions (continued)
Electric generation with dual fuel capability provides operating flexibility when NG supplies become limited due to unforeseen events
A disruption to one of the two major pipelines, lasting more than a few days could exceed liquid fuel supply capability
FRCC to review long term gas transportation adequacy with its entities
32

## Slide 33: FRCC Transmission Planning
33

## Slide 34: FRCC Regional Transmission Planning Process
Promote the reliability of the Bulk Electric System through coordination of transmission planning activities within the FRCC Region
Assess transmission adequacy and resource deliverability
34

## Slide 35: Crystal River Unit Retirements
2012 FRCC Long Range Study w/ CR 1, 2, and 3 online beyond 2015 showed FRCC grid reliable and secure for TY horizon
Subsequent FRCC evaluation of the retirement of CR3 and the potential 2015 retirements of CR 1 and 2 indentified:
  Transmission reliability issues impacting multiple entities starting in 2015 w/ no transmission alternatives available for 2015
  MATS compliance options under evaluation that would allow CR 1 and 2 to run for a limited period of time and resolve transmission issues
  Other transmission and generation alternatives under evaluation for 2016 and beyond
35

## Slide 36: Status of Compliance with FERC Order 1000
FERC jurisdictional entities have the obligation
Expand FERC Order 890 with regard to regional and inter-regional planning and cost allocation
Develop regional planning and cost allocation provisions
  10/11/2012 Initial Compliance filing
  6/20/2013 FERC issues order
  8/29/2013 Florida sponsors requested 90 day extension
  10/18/2013 Conforming Compliance filing
Develop inter-regional transmission coordination procedure and address cost allocation for multi-regional projects
  7/10/2013 Compliance filing
  Pending FERC Order
36

## Slide 37: Conclusion
Planned Reserve Margin exceeds 20% for all peak periods for the next ten years (although resource mix is changing towards greater dependence upon DSM resources)
Energy production from natural gas expected to increase 13.2% by 2022
Current pipeline capacity is 96% subscribed
FRCC to review long term gas transportation adequacy with its entities
37

## Slide 38: Conclusion (continued)
Impact of EPA regulations:
  RICE rule projected to negatively impact Demand Response projections for Commercial/Industrial participants
  Prospective 2015 retirements at Crystal River due to MATS would have transmission impacts
  Mitigation plans are being developed
38

## Slide 39
Questions ?